## Slide 1
Fire Assessment: Overview and Introduction

## Slide 2
Course Outline
3 to 4 hour course.
Designed for BCWS staff, contract crew leaders and forest industry personnel.
Recognized as the minimum training for fire assessment by firefighters.
Evaluation Criteria:
- Written Exam worth 70 %.
- Fire Assessment Activity 30 %.

## Slide 3
Learning Objective
Upon completion of this course, the trainee will develop the working knowledge and the ability required to complete and deliver an accurate fire assessment.
Observe the Fire

## Slide 4
Introduction to Fire Assessment
You will learn:
What a fire assessment is.
When a fire assessment is done.
Why a fire assessment is done.
Who performs a fire assessment.
A Fire Assessment versus An Initial Fire Report (IFR).
Who receives a fire assessment.

## Slide 5
Wildfires in British Columbia
Over the past 10 years:
There have been 2000 wildfires per year.
Burn close to 115000 hectares (ha).
61 % caused by lightning.
39 % are human caused.

## Slide 6
The 10 AM Concept

## Slide 7
Importance of Assessment
Wildfires need to be reported to BCWS staff promptly.
A Fire Centre will send resources to wildfires.
Reporting and an accurate fire assessment are critical to the 10 AM Concept.

## Slide 8
What is Fire Assessment?
Fire assessment is an ongoing process that includes:
All values at risk.
Present and expected fire behaviour.
Fuels, weather and topography.
Fire potential and best plan for suppression.
Resources required for suppression.
Fire hazards and crew safety issues.

## Slide 9
Upon arrival at a fire.
For any changes in fire behaviour or weather conditions.
When a set update is required.
When a supervisor needs to know the suppression progress.
When are Fire Assessments Done?
Increase in Fire Behaviour

## Slide 10
Regional Wildfire Coordination Officers (RWCOs).
Zone Wildfire Coordination Officers (ZWCOs).
All wildfire personnel working on suppression.
Who Receives Fire Assessment Information?
The
ZWCO

## Slide 11
Fire Assessments are completed in order to:
Update the Fire Zone and Fire Centre.
Provide resource requests.
Establish priorities when there are multiple fires.
Allocate resources effectively.
Why are Fire Assessments Done?
Cabin
at Risk

## Slide 12
Initial Attack Crew Leaders.
Incident Commanders.
Air Patrol Officers.
Experienced Firefighters.
The quality of the assessment depends on fire experience.
Who Performs Fire Assessments?

## Slide 13
An IFR is done only once for a fire.
An IFR is the start of a fire assessment.
Fire assessments are continuous.
Assessments provide continuous information to the Fire Centre.
A Fire Assessment vs. An Initial Fire Report
IFR Pad

## Slide 14
Roles and Responsibilities

## Slide 15
The Assessor and Duty Officers
Fire Assessment:
  IC and IA Crew Leaders.
  Experienced Firefighters.
The RWCO and ZWCO:
  Duty Officers.
A Flare Up

## Slide 16
Experienced Firefighters
An IC may request an assessment by experienced personnel if:
A flare up occurs.
There are control difficulties.
There are values at risk.
There is a new wildfire in the area.
Assessment By Helicopter

## Slide 17
Be Prepared and Organized.
Be Thorough - perform a complete and on going reconnaissance (Recce).
Be Accurate - record all fire information.
Communicate - the fire information effectively.
Responsibilities While Completing an Assessment

## Slide 18
Before Arrival at the Fire
Obtain updated information about the fire behaviour.
Look at weather forecasts.
Travel using the route that gives the best vantage point.

## Slide 19
Upon Arrival at the Fire
Identify LACES and fire hazards.
Estimate the potential for fire growth.
Determine whether more resources are needed.
Establish priorities considering values at risk.

## Slide 20
After Initial Fire Size-Up
Start an informal Incident Action Plan:
  Objectives, Strategies and Tactics.
Investigate the fire cause.
Preserve the ignition point.
Keep the Duty Officers informed.

## Slide 21
Ongoing Fire Updates
Continuously re-assess the fire.
Adjust strategies and tactics as needed.
Request more resources if required.
Communicate hazards.
Ensure that fire suppression follows safety protocols.

## Slide 22
To compile all information about fires.
  from the IFRs and fire assessments.
To mentor less experienced fire personnel through the assessment process.
To deploy the resources necessary to meet suppression objectives.
To request additional support from the PWCC.
Responsibilities of the Duty Officers

## Slide 23
Multiple Fire Situations
The RWCO will determine wildfire suppression priorities after considering:
Values at risk.
Concerns identified by the Fire Zones.
All relevant wildfire information.
Where resources will be most effective.

## Slide 24
The Duty Officers will decide:
to Continue Fire Suppression.
  IC will run fire operations.
  Fire Centre will support.
to Stop Fire Suppression.
  If not in fire management plan or too dangerous.
  Wait for fire analysis.
When the Control Objectives Are Not Met
A Tactical Withdrawal

## Slide 25
Generally based on safety concerns.
Fire could be put into modified response.
The fire will be monitored.
Possible containment lines should be determined.
Trigger points for fire suppression are established.
Stopping Fire Suppression

## Slide 26
If you are completing a fire assessment:
Be aware of the weather and fire behaviour forecasts.
Be prepared for the assessment tasks.
Consider the assessment when determining objectives.
Keep crews safe with continuous updates - Lookouts.
Your Role and Responsibilities

## Slide 27
Fire Behaviour

## Slide 28
Forest Layers

## Slide 29
Forest Fuels

## Slide 30
The Fire Triangle

## Slide 31
Suppressing Wildfires

## Slide 32
Fire Behaviour Factors

## Slide 33: Factors Influencing Fire Behaviour
Fuel
Moisture
Size
Spacing
Load
Weather
Wind
Temperature
Relative Humidity (RH)
Precipitation
Topography
Slope
Aspect
Terrain
Elevation

## Slide 34
Fuel
Moisture - refers to the water content within forest vegetation.
  Most critical fuel factor.
  Dead and dry fuels ignite more readily.
Size - heavy, slow burning or light, fast burning.
Spacing - Horizontal and Vertical fuels.
Loading - accumulation or mass of fuels in a given area (tons/hectare).

## Slide 35
Sample Fuel Types

## Slide 36
Weather
Wind - pushes wildfires into new fuels.
  Most critical weather factor.
  Dries out fuels and causes spotting.
Precipitation - rain increases fuel moisture content.
Relative Humidity (RH) - the percent of water vapour in the air.
Temperature - preheats fuels and decreases the RH.
Erratic wind will cause severe fire behaviour.

## Slide 37
The 30/30 Crossover Concept

## Slide 38
Topography
Slope - fire spreads rapidly on steep slopes.
  Most critical topography factor.
  Upslope fuels are closer to flames.
Aspect - South facing slopes get more direct sunlight.
Terrain - many natural features will funnel wildfires.
Elevation - warm air is trapped at low levels.
Steep, South facing slopes will have increased fire behaviour.

## Slide 39
‘Chimney Effect’
Gullies, Valleys and Canyons

## Slide 40
Thermal Belts

## Slide 41: The Canadian Forest Fire Danger Rating System (CFFDRS)
This system is used to determine:
Potential fire behaviour.
Fire spread rates.

## Slide 42: The CFFDRS
Is a standard national fire danger rating system.
Preparedness based on fire potential and fire spread rates.
2 sub-systems include:
  Fire Weather Index (FWI) System.
  Fire Behaviour Prediction (FBP) System.

## Slide 43: Fuel Moisture Codes
There are 3 fuel moisture codes used in the FWI.
Code | Represents | Time Lag * | Amount of 24 hour rainfall required to lower value
FFMC: Fine Fuel Moisture Code | Surface litter | 2/3 day | 0.6 mm
DMC: Duff Moisture Code | 5 - 10 cm duff | 12 days | 1.5 mm
DC: Drought Code | 10 - 20 cm duff | 52 days | 2.9 mm
* Time lag refers to the time required for fuel to lose 2/3 of its moisture under standard drying conditions.

## Slide 44
Fine Fuel Moisture Code
Litter, twigs, grass and other small cured fuels.
Affected by wind, temperature, rainfall and RH.
CODE / INDEX | INTERPRETATION
FFMC Less than 77 77 - 86 More than 86 Greater than 94 | Generally a fire will not start without a concerted effort. Approximately 50 % of ignition sources will start fires. Easy ignition of forest fuels. Almost 100 % of ignition sources will ignite forest fuels.

## Slide 45
Duff Moisture Code
Duff layer is 5 - 10 cm deep.
Includes medium sized woody material.
Affected by rainfall, temperature and RH.
CODE / INDEX | INTERPRETATION
DMC Less than 35 | Do not expect a great deal of involvement of fire in this layer. Expect more intense fires if above this level.

## Slide 46
Drought Code
Deep duff layer is 10 - 20 cm deep.
Includes roots and logs.
Affected by rainfall and temperature.
Seasonal drought increases DC substantially.
CODE / INDEX | INTERPRETATION
DC 0 - 300 300 - 450 500 + | Very little involvement of this fuel on most fires. Increased involvement with fires becoming more intense and mop-up problems increasing. Extensive involvement of the fuel layer. Fires are intense with difficult mop-up problems due to the depth of the fires.

## Slide 47: Fire Behaviour Indices
ISI: Initial Spread Index
  The fire spread rate immediately after ignition.
BUI: Build Up Index
  The amount of fuel available for consumption.
FWI: Fire Weather Index
  Potential fire intensity.
  Fire danger levels.
Fire
Spreading . . .

## Slide 48
The Fire Weather Index (FWI)

## Slide 49: The Red Book
All values are input into the FBP Red Book.
Fire behaviour can be predicted using the outputs.

## Slide 50
Fire Types

## Slide 51
Parts of a Fire
Head
Back/Heel
Flank
Finger
Bay
Island

## Slide 52
Fire Intensity Rank

## Slide 53
Hazards of intense fire behaviour.
The 3 factors influencing fire behaviour.
Fuel moisture, wind and slope issues.
The 4 Fire Types.
The 6 Fire Intensity Rankings.
What You Need to Know for Fire Assessments

## Slide 54
Questions?

## Slide 55
Preparing for a Fire Assessment

## Slide 56
Daily Preparation Requirements
Determine current fire behaviour in the zone.
Examine weather forecasts.
Know current resource availability.
Have the equipment and materials for fire assessment ready.
Portable Weather Station

## Slide 57
Temperature, RH and Wind Speed are key.
Weather stations provide FWI at 13:00.
Use the nearest weather stations.
Track cold fronts and thunderstorms.
Ask for fire behaviour advisories.
Daily Fire Weather and Fire Behaviour Forecasts

## Slide 58
Ask about the fire behaviour on local wildfires.
Discuss suppression difficulties on these fires.
Monitor the radio for changes in fire activity.
Talk to firefighters already in the field.
Current Fire Behaviour in the Area

## Slide 59
Helicopters.
Air Tankers.
Heavy Equipment.
Specialty Crews - Para Attack and Rappel.
Sustained Action Crews.
Water Tankers and Tenders.
Resources Available and Capabilities
Para Jumping Wildfire

## Slide 60
Maps of the Fire Zone and access routes.
Pens, pencils and ruler.
Clipboard with paper.
Ticker or flagging tape.
A handheld GPS unit.
An IFR pad (FS 260).
A weather kit.
Equipment and Materials Required

## Slide 61
CFFDRS FBP System Field Guide or Red Book.
Digital camera with extra batteries and memory card.
A completed IFR.
Vegetation Resource Inventory (VRI) maps of the fire area.
Helpful Fire Assessment Tools

## Slide 62
Examine any topographic or vegetation maps of the area.
Become as familiar with this location as possible.
Start any paperwork necessary - including the IFR.
Review the weather forecasts.
Predict the expected fire behaviour.
Watch for public in the area - potential cause.
On Route to the Fire

## Slide 63
Questions?

## Slide 64
Conducting the Fire Assessment

## Slide 65
This section will explain the following:
General consideration when conducting a fire assessment.
Initial communications to the Fire Centre.
Transmitting the IFR to Dispatch.
How to do fire reconnaissance (‘Recce’).
Completing the Initial Fire Report.
The Fire Assessment.
Conducting the Fire Assessment Topics

## Slide 66
Remain calm.
Check your location - on the right fire.
Use common sense during the Size Up.
Use Adaptive Management - re-evaluate the situation.
Do not avoid decisions.
Communicate - the fire assessment information to the Fire Centre and crews.
General Considerations

## Slide 67
Immediately notify the Fire Centre Dispatch once on site.
Provide a rough geographic location.
Do not wait until the IFR is complete.
Provide a basic fire assessment if possible (smoke and terrain).
Initial Communications

## Slide 68
“Prince George Fire Centre. Prince George Fire Centre. This is NIFAC 72 Alpha with a fire report. Are you ready to copy?”
Wait for response and then continue...
“I have located a small (or large), fast (or slow) moving wildfire 1 kilometer north of Gwillim Lake, approximately 300 meters west of a Forest Service Road. It is putting off white smoke.”
“Please standby for an IFR and fire assessment.”
Sample Radio Transmission

## Slide 69
Will be completed upon arrival at a wildfire.
Can be done from the air or by ground on approach.
Observe the fire activity and fuels.
Observe the surrounding environment.
Fire Reconnaissance or ‘Recce’

## Slide 70
Brief the pilot about assessment objectives.
The assessor must have best view of the fire.
Observations need to be noted - written.
Take photos or direct a crew member to if possible.
Recce from an Aircraft

## Slide 71
1st Pass - High:
At altitudes of 1000 to 2500 feet.
Try to observe the whole fire.
2nd Pass - Low:
At 150 to 300 feet - avoid fanning fire with rotor wash.
Identify specific factors about the area.
Completing Aerial Observations

## Slide 72
Note the following when completing a Recce:
Details about fuel types and topography.
Helicopter and vehicle access points.
Nearby water sources.
Description of any vehicles in the area.
Low Level Observations

## Slide 73
Stop the vehicle at a good vantage point.
Observe the fire characteristics.
Determine the fire activity and terrain features.
Note any water sources on route.
Maintain a view on approach if possible.
Recce from a Vehicle

## Slide 74
First document completed for a wildfire.
Communicated to the Fire Centre.
Divided using the phonetic alphabet.
  Makes for easier communication.
Crew Leaders can copy IFR from Dispatch.
  If not 1st on scene.
The Initial Fire Report (IFR)

## Slide 76
Name, Date and Time.
Geographic Location - a brief description.
Coordinates - Lat. and Long.
Elevation.
Ask the Fire Centre for an Incident Number.
To Start an IFR

## Slide 77
Alpha - Size
1. Single Tree
2. Spot m x m Less than 10 m by 10 m
3. 0.1 - 0.2 or the size of an IA truck.
4. 0.3 - 0.5 0.5 ha = 100 m x 50 m
5. 0.6 - 1.0 1.0 ha = 100 m x 100 m
6. 1.1 - 2.0 2.0 ha = 100 m x 200 m
7. 2.1 - 4.0
8. 4.1 - 8.0 5.0 ha = 200 m x 250 m
9. Other ha

## Slide 78
Linear Comparison
Use a map to check the length of:
  a lake.
  a runway.
  the distance between 2 roads.
Compare this distance with the length of a fire flank.
Tree heights can be useful on smaller fires.
Size and Distance Estimation

## Slide 79
To determine distance on the ground you must:
Have the pilot set up the aircraft to fly at a pre‑determined speed.
Time the aircraft as it flies between 2 points in the fire area.
Calculate the length of the flight path by:
  Converting the times, and multiplying the speed by the time.
  Multiplying to get the proper units (meters, kilometers).
Size and Distance by Flight Time

## Slide 80
To calculate fire size you must:
Visualize the fire as a square, rectangle or triangle.
Fly along and measure the distance of 1 side (length) and 1 end (width) of the fire.
Measure the height and base for triangle shaped fires.
Calculating Size

## Slide 81
Fire Size by Flight Time

## Slide 82
Speed = 180 km/h
Flight time for length = 40 seconds
Flight time for width = 20 seconds
180 km/h = 50 m/sec x 40 seconds
= 2000 metres
180 km/h = 50 m/sec x 20 seconds
= 1000 metres
Sample Fire Size Calculations

## Slide 83
Area of a 4‑sided object =
Length x Width
2000 m x 1000 m = 2000000 m2
2000000 m2  10000 m2 = 200 ha
A single hectare is 10000 square metres (100 m x 100 m).
Sample Fire Size Calculations

## Slide 84
Bravo - Fire Rank
1. Rank 1, Smouldering Ground Fire
2. Rank 2, Open Flame, No Spread
3. Rank 3, Vigorous Surface Fire, Moderate Spread, May See Candling
4. Rank 4, Moderate to Fast Spread, Short Aerial Bursts, Spotting
5. Rank 5, Continuous Crown Fire, Spotting Distance m
6. Rank 6, Continuous Crown Fire, Blow-up

## Slide 85
Charlie - Fuels
1. Grass
2. Brush
3. Deciduous
4. Slash
5. Reproduction
6. Open Timber
5. Heavy Timber
6. Other ____
7. FBP Type ____

## Slide 86
1. Life/Property ___________________
2. Timber (Forest) Resources (Including Reproduction) _
3. Other Special Values (Watersheds, Parks) ___
4. Distance ____ _ m N S E W of fire
Delta - Values at Risk (Immediately Threatened)

## Slide 87
Echo - Wind
1. Calm
2. Speed km/h
3. Direction N S E W
Calm Smoke is rising straight up.
1 to 15 km/h Smoke fans and bends slightly from a vertical to a horizontal.
16 to 30 km/h Smoke flows with the wind direction.
30 to 74 km/h Smoke flows parallel to ground and fire activity increases.
75 + km/h Wind storms pushing the fire in new directions and fire will be out of control.

## Slide 89
Foxtrot - Adjacent Fuels
1. Grass
2. Brush
3. Deciduous
4. Slash
5. Reproduction
6. Open Timber
5. Heavy Timber
6. Other ____
7. FBP Type ____

## Slide 90
Golf - Slope
1. Flat/Rolling
2. Moderate < 30 %
3. Steep > 30 % < 60 %
4. Extreme > 60 %
10 % slope ‑ 1 metre of vertically rise for every 10 metres of horizontal distance.
50 % slope ‑ 1 metre of vertical rise for every 2 metres of horizontal distance.
100 % slope - 1 metre of vertical rise for every 1 metre of horizontal distance.

## Slide 91
Hotel - Aspect
1. North
2. South
3. East
4. West
South and southwest aspects get the most direct sunlight.
Have fine, flashy fuels
Fuels dry out rapidly.
These slopes have increased fire activity.

## Slide 92
India - Slope Position
1. Bottom
2. Lower Third
3. Middle Third
4. Upper Third
5. Top
Position on a slope will indicate fuel type.
The position also dictates fire potential.
In addition, slope position serves as a location reference.

## Slide 93
Juliet - Access
1. Road __ __ m
2. Heli-spot __ __ m
3. Hover Exit _ ___ m
4. Other __ __ m
5. N S E W of the fire
The distance and direction from the fire should be noted.
Natural or constructed openings make good heli-spots.
Large clearings can be used as ‘staging areas.’

## Slide 94
Kilo - Available Water
1. None
2. Adjacent
3. ________ m N S E W of the fire
The availability of water and proximity to the fire will determine water delivery.
Indicate the source and potential supply issues.
Patches or a string of deciduous growth, tamarack or hemlock indicate a water source.

## Slide 95
Lima - Paper Trailed and
Mike - Photos
1. Yes
2. No
All initial attack wildfires can be paper trailed.
Allows ground crews to find the fire with ease.
Photos are valuable for fire behaviour analysis and fire cause investigation.
Photos of the point of origin are key.

## Slide 96
November - Suspected Fire Cause
1. Human
2. Lightning
Determining the cause of the fire is extremely important
Helps Fire Centre staff when billing for the incident.
If it is a human caused fire, the point of origin should be barricaded.

## Slide 97
Actions Taken/Recommended
This section should not be overlooked.
Relay this information.
Describe resources committed and suppression progress.
Determine probability of success.

## Slide 98
From the Fire Centre.
Resources will be requested for this incident number.
The IFR will be filed under this number.
Serves as identification for all reports.
The Incident Number

## Slide 99
Contact the Fire Centre by radio.
Wait until the dispatcher is ready.
Communicate the location and fire number.
Speak in a clear and concise manner.
Ask for the dispatch to repeat information.
Ask for feedback.
Communicating the IFR to the Fire Centre

## Slide 100
The Fire Assessment
Communicating What You See

## Slide 101
Update the Fire Centre with relevant information.
Provide a summary of fire suppression activities:
  Firefighters and equipment on site.
  Control line locations and types.
  Resources required.
  Control problems (resistance to control).
  Anticipated time of control.
  Recommended action in the event of initial attack failure.
Fire Assessment Checklist

## Slide 102
3. Safety Concerns
  Fire Hazards, Danger Areas , LACES, Check-Ins, etc.
4. Resource Request Considerations
  Determining the resources required to suppress a fire.
  Fundamental task of assessment.
  The following points need to be addressed:
Fire Assessment Checklist

## Slide 103
Attempt to meet the control objectives:
  By the next day’s burning period.
  Assessments are key to decision making.
Anticipate fire behaviour.
  Be flexible with resources.
  Do not expect help.
Resource Request Considerations
Control Line
Needs

## Slide 104
Make your resource requests complete.
  Consider all equipment and machines needed.
  Ensure resources arrive with appropriate tools.
Fight the fire aggressively.
  If more resources are needed for suppression, ask.
  Do not overwork crews - get more personnel.
  BE SAFE!
Resource Requirements

## Slide 105
Determine elevation changes from water source to fire.
Calculate number of pumps needed.
Locate helicopter and water tender access sites.
Remember, water is used most effectively with a nozzle person and a grubber.
Ask for foam!
Estimating Water Delivery Resources
Bladder
Site

## Slide 106
Availability - time to arrive at fire and access.
Machine ability - terrain.
Environmental sensitivity.
Number of machines.
Line locators - 2 per flank.
Burn out and suppression crews.
Line resistance, fuel loading and time of day.
Estimating Heavy Equipment Resources
Equipment Staging

## Slide 107
Fire crews and heavy equipment need to work together.
Many saw operators and swampers are needed in slash and blow down.
Steep slopes will slow down progress.
Rocky or swampy ground hinders suppression.
Control Line Resistance
Hand
Guard

## Slide 108
Air Tanker Requests

## Slide 109
An air tanker request takes time.
Are very helpful on IA fires.
Can be used during fire busts with multiple starts.
Air tankers aid in suppressing the fire perimeter.
An alternative is helicopter support.
If air tankers are needed, ask immediately.
Air Tanker Requirements

## Slide 110
A firefighter must consider the following prior to asking for air tankers:
Access issues for aircraft.
The current fire behaviour.
The fuel moisture code and fire behaviour indexes.
The weather forecasts.
Before Making the Request

## Slide 111
If rates of spread are high, air tankers will have limited effect.
Air tankers work well on low intensity fires.
Crews often need retardant support.
Air tankers will slow down a wildfire.
Firefighters need to continue to working.
Consider the Rate of Spread
Slash Fire

## Slide 112
Air Tankers vs. Helicopters
The choice to use helicopters is based on the following:
Effectiveness with current fire behaviour.
Productivity compared to an air tanker.
The turn around time to an adequate water source.
Need for crew transport services.

## Slide 113
Sample of Tanker Drops vs. Bucketing
Intermediate Helicopter - 210 gallons x 10 turnarounds/hour
= 2100 gallons of water or foam per hour
Land Based Air Tanker - 3300 gallons x 1 drop/hour
= 3300 gallons of retardant, water or foam per hour
6 minute turnaround for the helicopter.
1 hour turnaround for the air tank.

## Slide 114
The Fire Sketch

## Slide 115
Helps to visualize and interpret the entire fire.
A copy can aid the Duty Officers in setting priorities.
Provides rough bearings and significant features.
Can be useful when estimating fire size.
Needs to be completed after a ground ‘Recce.’
Purpose of the Fire Sketch

## Slide 116
An Accurate Fire Sketch

## Slide 117
Use a blank piece of plain paper.
Determine items to be recorded on either side - a map legend.
List topographical features.
Draw a North arrow on the sketch paper.
Draw numerous easily identifiable features on the sketch with approximate relation to North, South, East or West.
Fire Sketch Guidelines

## Slide 118
The Basics
N
Water
Road
Fuels

## Slide 119
Draw the fire perimeter.
Make note of water sources, control lines, natural breaks, fuels, etc.
Mark the estimated distance to all relevant features.
It will take several ‘Recce’s’ to complete an accurate sketch.
Outlining the fire perimeter on a topographical map is also effective.
Fire Sketch Guidelines

## Slide 120
Fire Sketches can be Replaced with Maps
Project Fires

## Slide 121
Complete a thorough ‘Recce’ at a new wildfire.
Communicate initial finding to the Fire Centre Dispatch.
Fill out an IFR and do a Fire Assessment.
Follow the fire assessment checklist.
Request adequate resources.
Continuously update the Fire Centre with situation reports.
Your Role and Responsibilities in Fire Assessment

## Slide 122
Questions?

## Slide 123
Fire Assessment Activity

## Slide 124
Study the following fire information.
Examine the fire assessment checklist from the trainee manual.
Note all relevant fire information observed in the photos.
Complete an IFR provided by the instructor or the sample form from the manual.
Complete a sketch of the fire based on the photos.
Fire Assessment Activity

## Slide 125
Today’s Fire Behaviour and Weather Forecast (July 7)
Fuel Moisture Codes and Forecasted Indices
FFMC: 90, DMC: 128, DC: 480
BUI: 158, ISI: 6
FWI: 27.4
Weather
Temperature 32 C, RH 30 %
Wind: SW - 5 km/h
Precipitation: 0.0 mm

## Slide 126
Tomorrow's Fire Behaviour and Weather Forecast (July 8)
Fuel Moisture Codes and Forecasted Indices
FFMC: 93, DMC: 134, DC: 489
BUI: 162, ISI: 18
FWI: 57.3
Weather
Temperature 31 C, RH 23 %
Wind: S - 15 to 20 km/h
Precipitation: 0.0 mm

## Slide 127
Fuel Type and Fire Behaviour
Sample Fuel Type: C-5 Fire Behaviour

## Slide 128
Smoke on Approach - 25 KM
N

## Slide 129
A Helicopter Circling 2.5 KM from the Wildfire
N

## Slide 130
N
Low Level Pass - 5 km/h Winds

## Slide 131
Low Level Pass - Calm Winds
N

## Slide 132
High Altitude Pass - Gusting Winds from Lake
N

## Slide 133
High Altitude Pass - Gusting Winds from Lake
N

## Slide 134
IFR and Fire Assessment Exercise
Select another trainee as your partner.
1st Communication - provide the Fire Centre (your partner) with a complete IFR including actions recommended.
Individually complete a full fire assessment using forecasts from slides.
2nd Communication - update the Fire Centre with a complete Fire Assessment and discuss concerns with your partner.
View the final photos of the fire and hand in assessment.

## Slide 135
Fire Activity by 1530 - 2.5 Hours After IFR
N

## Slide 136
Fire Behaviour at 1600 - 3 Hours After IFR

## Slide 137
Fire Activity by 1730 the Following Day
N

## Slide 138
Fire Behaviour by 1500 on the Third Day of Burning

## Slide 139
Fire Environment during Fifth Day of Burning

## Slide 140
Questions?