## Slide 1: NIMC Hazard Assessment & Abatement
Forestry Management Leadership Team
Port McNeil l - October 22, 2013
Pete Laing, RFT – Quinsam Fire Base

## Slide 2: Hazard Assessment and Abatement
Intro – experience & certification
Intro - opinion, professional obligations, official obligations
Presentation overview – Coastal Fire Centre overview, statutory obligations/interpretations, assessment, best practice, abatement
Context/perspective; interpreting law into appropriate actions
Weather stations statutory obligations & options
Comments, questions and discussion

## Slide 3: Coastal Fire Centre Overview
Current practice, guidance and approaches are being reviewed Regionally and Provincially
Coastal fuel types are being reviewed (FBP)
Coastal has identified concerns with some practice (assessment & abatement) within Fire Centre boundaries
Resource Management Burn Plans

## Slide 4: OBSCR
New legislation has stalled; release for fall 2013 pushed back
Less restrictive regulations potentially in secondary zones
Primary zones likely staying the same or possibly more restrictive

## Slide 5: Statutory Obligations
The Wildfire Act & Reg.
Professional Reliance/results based
Prescriptive requirements
Qualified holders

## Slide 6: HAZARD ASSESSMENT
Wildfire Reg. states that hazard assessment must be completed;
  Every 3 months while operating within, or within 2 km, of local government boundaries as defined in the WA (Interface) – WR 11(2)
  6 months everywhere else – WR 11(3)
  Option for qualified holder to complete assessments as specified by an RPF or RFT (rationale required) – WR 11(3.1)(b)

## Slide 7: HAZARD ASSESSMENT
Hazard assessments must include assessment of fire hazard and risk of fire starting/spreading
– WR 11(4)(a)

## Slide 8: HAZARD ASSESSMENT
A person must abate fire hazard to levels that are not greater then prior to harvesting operations – WR 12(2)(a)(b) & 12.1(3)(i)(ii)
  Or, In the case of a qualified holder as specified by a RPF or RFT (with rationale) – WR 12.1(3)(b)

## Slide 9: HAZARD ASSESSMENT
An official may identify circumstances they consider constitutes a fire hazard and by written order may require applicable person to abate said fire hazard by a specified date. The person who is subject to this order must comply – WA 7(3) and 7(4)

## Slide 10: HAZARD ASSESSMENT
Scope of Practice – competent/qualified; experience, training, knowledge
Due diligence – rationale, peer review
Professional disagreement/accountability
Common sense, best practice, best science

## Slide 11: HAZARD ASSESSMENT
Exemptions – comprehensive fuel management plan
Exemptions – wet belt, other
Develop alternate assessment processes
FPB 2008 special Inv.

## Slide 12: Guidance

## Slide 13: Risk Map

## Slide 14: Schedule 7

## Slide 15: Schedule 7

## Slide 16: Best Practises

## Slide 17: 1. Woody Debris Management Strategies

## Slide 18: 2. Harvesting

## Slide 19: 3. Harvesting Methods

## Slide 20: Secondary Tenures
Crown land only
Tenure limited to smaller area of operation within block

## Slide 21: 4. Alternatives to Open Burning

## Slide 22: 5. Alternatives to Open Burning

## Slide 23: 6. Alternatives to Open Burning

## Slide 24: 6. Alternatives to Open Burning

## Slide 25: 7. Best Practice – Debris Piling

## Slide 26: 8. Best Practice – Debris Piling

## Slide 27: 9. Open Burning
Wildfire Act & Reg
Environmental Management Act (EMS)
Open Burning Smoke Regulation (OBSCR); venting
Regional Districts & Municipal Jurisdiction; Bylaws
Category 3; Reg. #
Resource Management Burn; Reg. #

## Slide 28: 9. Open Burning

## Slide 29: 10. When to Burn (FWI)

## Slide 30: 10. When to Burn (FWI)
Safe conditions to burn & continuing to be safe
Weather Forecast
Venting Forecast
  Environment Canada
  Custom

## Slide 31: 11. When to Burn/Venting Index

## Slide 32: 12. Notifications Prior to Burning
Public media campaign – radio/newspaper?

## Slide 33: 12. Notifications Prior to Burning

## Slide 34: 13. Burn Checklist

## Slide 35: IF YOU BUILD IT; BURN IT!!!

## Slide 36: Weather Stations
Ensure representative weather station for industrial operations. WR 6(2)(a)
Option 1 – WMB rental. $3000 per year rental, plus extraordinary costs (heli)
  Set up
  Data
  Forecast
  Equipment availability dependant

## Slide 37: Weather Stations
Option 2 – purchase Similar WMB hardware. $16,000 + -
Option 3 – purchase from a multitude of small portable stations.
  $1000 to $20,000
  start up codes
  Software; coming soon CFS online software

## Slide 38: QUESTIONS?